## Slide 1: Locomotive Safety Standards Part 229
Subpart A – General
Module 2

## Slide 2: Module Objectives
Module 2
<number>
List conditions associated with the movement of a non-complying locomotive for repair
Recognize a properly completed tag for movement of a non-complying locomotive for repair

## Slide 3: Subpart A Overview
Module 2
<number>
General:
229.01 - Scope 
229.03 - Applicability 
229.04 - Information collection
229.05 - Definitions 
229.07 - Prohibited acts 
229.09 - Movement of non-complying locomotives 
229.11 - Locomotive identification 
229.13 - Control of locomotives 
229.14 - Non-MU control cab locomotives 
229.17 - Accident reports 
229.19 - Prior waivers
Notes: <number>

## Slide 4: Applicability
Module 2
<number>
Part 229 applies to all standard gage railroads operating on the general system of railroad transportation.

## Slide 5: Exemptions
Module 2
<number>
Part 229 does not apply to:
A railroad that operates only on track inside an installation which is not part of the general railroad system of transportation.
Rapid transit operations in an urban area that are not connected with the general railroad system of transportation.

## Slide 6: Additional Exemptions
Module 2
<number>
Locomotives used in passenger service are conditionally exempt from the following sections:
§229.125 – Headlights & auxiliary lights, (Tier II equipment only).
§229.141 – Body structure, MU locomotives.

## Slide 7: Definitions
Module 2
<number>
There are several definitions listed in this rule, we will discuss only those definitions that may impact your understanding of what we’ll be attempting to impart to you this week.

## Slide 8: Cab
Module 2
<number>
Means that portion of the superstructure designed to be occupied by the crew operating the locomotive.

## Slide 9: Control Cab Locomotive
Module 2
<number>
Means a locomotive without propelling motors but with one or more control stands.

## Slide 10: Dead Locomotive
Module 2
<number>
Means a locomotive other than a control cab locomotive that does not have any traction device supplying tractive power, or a control cab locomotive that has a locked and unoccupied cab.

## Slide 11: Event Recorder
Module 2
<number>
Means a device, designed to resist tampering, that monitors and records data on train speed, direction of motion, time, distance, throttle position, brake applications and operations (including train brake, independent brake, and, if so equipped, dynamic brake applications and operations) and, where the locomotive is so equipped, cab signal aspect(s), over the most recent 48 hours of operation of the electrical system of the locomotive on which it is installed. A device, designed to resist tampering, that monitors and records the specified data only when the locomotive is in motion shall be deemed to meet this definition provided the device was installed prior to May 5, 1995, and records the specified data for the last eight hours the locomotive was in motion.

## Slide 12: High Voltage
Module 2
<number>
Means an electrical potential of more than 150 volts.

## Slide 13: Lite Locomotive
Module 2
<number>
Means a locomotive or a consist of locomotives not attached to any piece of equipment or attached only to a caboose.

## Slide 14: Locomotive
Module 2
<number>
Means a piece of on-track equipment other than hi-rail, specialized maintenance, or other similar equipment in combination of, or with any of the following:
One or more propelling motors designed for moving other equipment.
One or more propelling motors designed to carry freight or passenger traffic or both.
Without propelling motors but with one or more control stands.

## Slide 15: Modesty Lock
Module 2
<number>
Means a latch that can be operated in the normal manner only from within the sanitary compartment, that is designed to prevent entry of another person when the sanitary compartment is in use. A modesty lock may be designed to allow deliberate forced entry in the event of an emergency.

## Slide 16: MU Locomotive
Module 2
<number>
Means a multiple operated electric locomotive as described below:
One or more propelling motors designed to carry freight or passenger traffic or both, or
Without propelling motors but with one or more control stands.

## Slide 17: Other short-haul passenger service
Module 2
<number>
Means the type of railroad service described under the heading "Other short-haul passenger service" in 49 CFR part 209, Appendix A.

## Slide 18: Potable Water
Module 2
<number>
Means water that meets the requirements of 40 CFR part 141, the Environmental Protection Agency's Primary Drinking Water Regulations, or water that has been approved for drinking and washing purposes by the pertinent state or local authority having jurisdiction. For purposes of this section, commercially available, bottled drinking water is deemed potable water.

## Slide 19: Powered Axle
Module 2
<number>
Means an axle equipped with a traction device.

## Slide 20: Sanitary
Module 2
<number>
Means lacking any condition in which any significant amount of filth, trash, or human waste is present in such a manner that a reasonable person would believe that the condition might constitute a health hazard; or of strong, persistent, chemical or human waste odors sufficient to deter use of the facility, or give rise to a reasonable concern with respect to exposure to hazardous fumes. Such conditions include, but are not limited to, a toilet bowl filled with human waste, soiled toilet paper, or other products used in the toilet compartment, that are present due to a defective toilet facility that will not flush or otherwise remove the waste; visible human waste residue on the floor or toilet seat that is present due to a toilet facility that overflowed; an accumulation of soiled paper towels or soiled toilet paper on the floor, toilet facility or sink; an accumulation of visible dirt or human waste on the floor, toilet facility, or sink; and strong, persistent chemical or human waste odors in the compartment.
Notes: <number>
Unsanitary means having any of these conditions present.

## Slide 21: Serious Injury
Module 2
<number>
Means an injury that results in the amputation of any appendage, the loss of sight in an eye, the fracture of a bone, or the confinement in a hospital for a period of more than 24 consecutive hours.

## Slide 22: Sanitation Compartment
Module 2
<number>
Means an enclosed compartment on a railroad locomotive that contains a toilet facility for employee use.

## Slide 23: Toilet Facility
Module 2
<number>
Means a system that automatically or on command of the user removes human waste to a place where it is treated, eliminated, or retained such that no solid or non-treated liquid waste is thereafter permitted to be released into the bowl, urinal, or room and that prevents harmful discharges of gases or persistent offensive odors.

## Slide 24: Transfer Service
Module 2
<number>
Means a freight train that travels between a point of origin and a point of final destination not exceeding 20 miles and that is not performing switching service.
Note: This definition applies only in the context of the sanitation section under Part 229.

## Slide 25: Washing System
Module 2
<number>
Means a system for use by railroad employees to maintain personal cleanliness that includes a secured sink or basin, water, antibacterial soap, and paper towels; or antibacterial waterless soap and paper towels; or antibacterial moist towelettes and paper towels; or any other combination of suitable antibacterial cleansing agents.

## Slide 26: Prohibited Acts
Module 2
<number>
This section essentially tracks the Locomotive Inspection Act language enacted by Congress. This section may be cited by inspectors when a locomotive is unsafe for use (emphasis added), but the defect cannot be linked with a specific section(s) within Part 229, other than §229.7.
This section also serves notice to any person, e.g., railroad/railroad employee or both, manufacturer, contractor, etc., may be subject to a civil penalty for violating or causing a violation of Part 229.

## Slide 27: Movement of Non-Complying Locomotives
Module 2
<number>
A locomotive defective under CFR Part 229 may move for repair only after a qualified person has made the following determinations:
The locomotive is safe to move, and
The maximum speed and other restrictions necessary for safely conducting the movement.
FRA or State MP&E Journeyman Inspector are authorized to impose additional restrictions for movement with a Form 8 (Special Notice for Repair).

## Slide 28: Conditions for Movement of Non-complying Locomotives
Module 2
<number>
A locomotive that develops a non-complying condition en route may continue in service until the next forward point where the necessary repairs can be made, or the next calendar day inspection, whichever occurs first.
Speed and other restrictions imposed by the qualified inspector or FRA must be observed.
The engineer and crew members shall be notified in writing of the restrictions (if any), and all non-complying conditions. Note: A copy of the non-complying tag discussed in the following slides will suffice.

## Slide 29: Non-complying Locomotives Tagging
Module 2
<number>
A tag bearing the words “non-complying locomotive” shall be securely attached to the control stand on each MU or control cab locomotive and to the isolation switch or near the engine start switch on every other type of locomotive. The information required on the tag shall contain the following: see next slide.

## Slide 30: Non-complying Locomotives Tagging - Required Information
Module 2
<number>
The locomotive number.
The name of the inspecting carrier.
The inspection location and date.
The nature of each defect.
Movement restrictions, if any.
The destination.
The signature of the person making the determinations required by this paragraph.

## Slide 31: Non-complying Locomotives Yard Moves
Module 2
<number>
A non-complying locomotive may be moved lite or dead within a yard, at speeds not in excess of 10 miles per hour, without meeting the requirements previously discussed, if the movement is solely for the purpose of repair.
Notes: <number>
Note: Under this circumstance, the carrier is responsible to insure that the movement may be safely made.

## Slide 32: Inoperative Locomotives
Module 2
<number>
A dead locomotive may not continue in use following a calendar day inspection as a controlling locomotive or at the head of a train or locomotive consist.
A locomotive does not cease to be a locomotive because its propelling motor or motors are inoperative or because its control jumper cables are not connected.

## Slide 33: Non-Complying Locomotive Exclusions
Module 2
<number>
The movement of defective locomotive provision (§229.9), does not apply to cab sanitation. The cab sanitation section has its own movement provisions.

## Slide 34: Special Notice for Repair
Module 2
<number>
Use only if you have reason to believe that the railroad will not take appropriate steps to insure safe movement of the car.
Use only if the defect is imminently hazardous and has the potential to cause a derailment, injury, death, or damage to property.
Contact your SPECIALIST when in doubt
Special Notice for Repair could be used to attach conditions for movement if you’re not satisfied with railroad imposed restrictions.
Notes: <number>
Key Points
Once again stress judicious use of the Special Notice for Repairs

## Slide 35: Movement of Non-Complying Locomotives
Module 2
<number>
Discussion and Movement for Repair Matrix

## Slide 36: Locomotive ID
Module 2
<number>
The letter “F” shall be displayed on each side of the locomotive to indicated which end is the front end.
The locomotive number shall be displayed on each side of the locomotive.
Notes: <number>

## Slide 37: Control of Locomotives
Module 2
<number>
Unless the locomotive is moving under the provisions of §229.9, whenever two or more locomotives are coupled in remote or multiple control, all the functions on the trailing locomotives shall respond to the actions from the cab of the controlling locomotive, e.g., sanders, air brakes, power, etc. If a dynamic brake or regenerative brake system is in use, that portion of the system in use shall respond to control from the cab of the controlling locomotive.

## Slide 38: Non-MU control cab Locomotives
Module 2
<number>
On each non-MU control cab locomotive, only those components added to the passenger car that enable it to serve as a lead locomotive, control the locomotive actually providing tractive power, and otherwise control the movement of the train, are subject to this part.
An example of these type locomotive include push-pull operations such as those utilized in Chicago commuter service, (Metra)..

## Slide 39: Accident Reports LAX Accidents
Module 2
<number>
Railroads are required to report serious injuries or death resulting from failure of a locomotive component or appurtenance, including electrocution.
This requirement applies to any locomotive (system & foreign), operated by the railroad.
The locomotive shall be preserved in tact by the railroad until inspected by FRA.
Notes: <number>
The report shall state the nature of the accident, number of persons killed or seriously injured, the place at which it occurred, the location at which the locomotive or the affected parts may be inspected by the FRA, and the name, title and phone number of the person making the call. Written confirmation of the oral report required by paragraph (a) of this section shall be immediately mailed to the Federal Railroad Administration, RRS-25, Washington, DC 20590, and contain a detailed description of the accident, including to the extent known, the causes and the number of persons killed and injured. The written report required by this paragraph is in addition to the reporting requirements of 49 CFR part 225.

## Slide 40: End of Module
Module 2
<number>