## Slide 1: Passenger Equipment Safety Standards Part 238
Subpart A – Movement of Defective Equipment
Subpart D - Brake Tests
Module 11
Notes: Module 11
<number>

## Slide 2: Module Objectives
Module 11
<number>
Apply FRA Safety Standards
Recognize deviations from the standards

## Slide 3: Subpart D - Overview
Module 11
<number>
238.301-Scope
238.303 - Exterior calendar day mechanical inspection of passenger equipment
238.305 - Interior calendar day mechanical inspection of passenger cars
238.307 - Periodic mechanical inspection of passenger cars and unpowered vehicles used in passenger trains
238.309 - Periodic brake equipment maintenance
238.311 - Single car test
238.313 - Class I brake test 
238.315 - Class IA brake test 
238.317 - Class II brake test 
238.319 - Running brake test 
Subpart A:
238.15 - Movement of passenger equipment with power brake defects 
238.17 - Movement of passenger equipment with other than power brake defects 
Notes: Module 11
<number>

## Slide 4: Class I Brake Test - 238.313 Commuter and Short & Long Distance Intercity
Module 11
<number>
Each calendar day
Long-distance intercity passenger trains at departure or originating terminal each calendar day or 1500 miles of continuous service whichever occurs first
A long distance, intercity passenger train that misses a scheduled calendar day Class I brake test due to a delay en route may proceed to the point where the Class I brake test was scheduled to be performed. A Class I brake test shall be completed at that point prior to placing the train back in service
Special consideration given to late night commuter trains (see matrix)
Notes: Module 11
<number>
Refer to brake test matrix
Class I is essentially a initial terminal brake test

## Slide 5: Class I Brake Test Adding Cars
Module 11
<number>
Each passenger car or unpowered vehicle added to a passenger train shall receive a Class I or Class 1A brake test unless written notice is provided to train crew that a Class I brake test was performed on the car within the previous calendar day and the car has not been off a source of compressed air for more than four hours prior to being added to the train
The written notice shall contain the date, time and location of the last Class 1 brake test

## Slide 6: Class I Brake Test Who & How?
Module 11
<number>
Class I brake test must be performed by a QMP
Class I brake test may be performed either separately or in conjunction with the exterior calendar day mechanical inspection
Class I brake test shall be performed at the air pressure at which the train will be operated, but not less than 90 psi
Unless the car or vehicle is moving under 238.15(b), 100 percent operative brakes are required on passenger trains receiving a Class I brake test
Brakes must be observed/inspected on both sides of car to verify application and release
Friction brakes must apply and remain applied until a release of the brakes has been initiated

## Slide 7: Class I Brake Test How?
Module 11
<number>
Check;
Brake shoes or pads aligned correctly, proper thickness and firmly seated against the wheel or disc,
Piston travel or actuator (within prescribed limits),
Communication signal system or two-way radio tested for proper operation,
Engineer’s brake valve or controller for proper operation,
Brake pipe leakage does not exceed 5 psi per minute if brake pipe leakage will affect service performance,
Emergency control devices (e.g. deadman pedal) function as intended,
Notes: Module 11
<number>
Does the emergency control device place train in emergency?

## Slide 8: Class I Brake Test How? - Continued
Module 11
<number>
Angle and cut-out cocks properly positioned,
Brake rigging does not bind or foul,
Electropneumatic brakes function as intended verified by walking each car,
Brake disks are free from cracks that exceed manufacturers specifications,
Brake indicators if so equipped operate as intended,
Brake pipe pressure changes are verified at the rear of the train.

## Slide 9: Class I Brake Test Records
Module 11
<number>
A written or electronic record shall be maintained of each Class I brake test performed and be provided to FRA upon request
This record shall be maintained at the place where the inspection is conducted or at one central location and shall be retained for at least 92 days.
The record must contain the following information;
  The date and time that the Class I brake test was performed,
  The location where the test was performed,
  The identification number of the controlling locomotive of the train,
  The total number of cars inspected during the test, and
  The signature or electronic identification of the inspector.

## Slide 10: Class IA Brake Test - 238.315 When?
Module 11
<number>
Prior to the first morning departure of each commuter or short-distance intercity passenger train unless a Class I brake test was performed in the previous 12 hours and the train has not been used in passenger service since the performance of the Class I brake test, and the train has not been off a source of compressed air for more than four hours since the Class I brake test was performed
Commuter or short-distance intercity passenger trains providing continuous late night service that began prior to midnight may forgo an additional brake test. However, trains in this type service shall receive Class I or Class IA brake test before starting a new daily operating cycle
If a Class IA brake test is performed at the start of the new daily operating cycle, the train must receive a Class I brake test at some point during the current calendar day
Notes: Module 11
<number>
Refer to brake test matrix

## Slide 11: Class IA Brake Test Who & How
Module 11
<number>
Class IA brake test must be performed by a QP or QMP
Class IA brake test shall be performed at the air pressure at which the train will be operated
Unless the car or vehicle is moving under 238.15 (b), 100 percent operative brakes are required on passenger trains receiving a Class IA brake test
Each brake must be observed/inspected to verify application and release if the railroad determines that the procedure is safe
If not safe, brake indicators may be used to determine the set and release on cars so equipped, but observation must be made by walking the train

## Slide 12: Class IA Brake Test How?
Module 11
<number>
Check;
Brake pipe leakage does not exceed 5 pounds per square inch per minute if brake pipe leakage will affect service performance,
Each brake sets and releases by inspecting in the manner previously described,
On MU equipment, the emergency brake application and the deadman pedal or other emergency control devices function as intended,
Each angle cock and cutout cock is properly set,

## Slide 13: Class IA Brake Test How? - Continued
Module 11
<number>
The communication of brake pipe pressure changes at the rear of the train is verified, which may be accomplished by observation of an application and release of the brakes on the last car in the train, and
Communication signal system or two-way radio tested for proper operation.

## Slide 14: Class II Brake Test – 238.317 When?
Module 11
<number>
All passenger trains whenever the control stand used to control the train is changed prior to the train's departure from the terminal complex with passengers
Prior to the first mornings departure of each commuter or short-distance intercity passenger train where the Class I brake test remains valid
Cars that have received a Class I brake test the previous calendar day, have not been off a source of compressed air for more then four hours and are added to a train
Cars or equipment are removed from a train
When operator first takes charge of train except in cases of face to face relief

## Slide 15: Class II Brake Test Who & How?
Module 11
<number>
Class II brake test must be performed by a QP or QMP
Except as provided in 238.15, a railroad shall not use or haul a passenger train in passenger service from a terminal or yard where a Class II brake test has been performed, or was required by this part to have been performed, with any of the brakes cut-out, inoperative, or defective

## Slide 16: Class II Brake Test How?
Module 11
<number>
Check;
The brakes apply and release at the rear of the train in response to signal from engineer’s brake valve or controller from leading or controlling unit, or a gauge or similar device at the rear of train or cab or the rear unit indicating brake pipe pressure changes,
On MU equipment, the emergency brake application and deadman pedal or other emergency control devices function as intended,
Communication signal system or two-way radio tested for proper operation.

## Slide 17: Running Brake Test – 238.319 When?
Module 11
<number>
After all passenger train departures as soon as conditions safely permit
All passenger trains whenever the control stand used to control the train is changed within a terminal complex and train is not in passenger service

## Slide 18: Running Brake Test How?
Module 11
<number>
The running brake test shall be conducted in accordance with the railroad's established operating rules, and shall be made by applying brakes in a manner that allows the engineer to ascertain whether the brakes are operating properly
If the engineer determines that the brakes are not operating properly, the engineer shall stop the train and follow the procedures provided in 238.15.

## Slide 19: Passenger Brake Test Discussion
Module 11
<number>
Refer to matrices

## Slide 20: Movement for Repair
Module 11
<number>
Two provisions for the movement of defective equipment;
Movement for repair with power brake defects – 238.15
Movement for repair with other than power brake defects – 238.17
  Both provisions have limitations and conditions that must be followed in order for movement to be allowed without civil penalty liability
  Both provisions essentially apply to Tier I equipment (certain sections of provisions apply to Tier II and are incorporated by reference, see 238.503 (e) & (f))
  Railroad not relieved of liability in the event of death or injury to railroad employee arising from movement of defective equipment referred to above
  Equipment defective under Part 229 used in passenger service will also be subject to restrictions imposed under Part 229.9
Notes: Module 11
<number>
20303 (c) Liability.--The movement of a vehicle under this section is at the risk only of the railroad carrier doing the moving. This section does not relieve a carrier from liability in a proceeding to recover damages for death or injury of a railroad employee arising from the movement of a vehicle with equipment that is defective, insecure, or not maintained in compliance with this chapter.
ASK TOM TO SPEAK ABOUT RESPONDSIBILITY FOR COMPLIANCE 238.9, e.g. Strict Liability vs. Reasonable Man Standard

## Slide 21: Movement for Repair with Power Brake Defects – 238.15
Module 11
<number>
At the time a Class I or Class IA brake test is performed movement may occur without civil penalty liability provided the following conditions are met;
Train moved for repair without passengers,
Applicable operating restrictions based on percent of operative brakes in train,
Defective equipment properly tagged or information recorded via automated tracking system,
Train moved without passengers for scrapping or sale, at speeds of 15 mph or less, and in accordance with railroad’s air brake or power brake instructions.

## Slide 22: Power Brake Defects - Enroute
Module 11
<number>
Enroute, after Class I or Class IA brake test is performed movement may occur without civil penalty liability provided the following conditions are met;
The brakes were operative at the Class I or Class IA brake test and became defective enroute
Applicable operating restrictions based on percent of operative brakes in train
Defective equipment properly tagged or information recorded via automated tracking system

## Slide 23: Power Brake Defects - Enroute Continued
Module 11
<number>
If the en route power brake defect causes the brake to be inoperative or cut-out, then the percentage of operative brakes on the train must be calculated.
Notify dispatcher of the percentage of operative brakes in train and movement restrictions
Notify mechanical department of the failure
Confirm the percentage of operative brakes by performing a walking inspection at the next location where the railroad reasonably judges that it is safe to do so

## Slide 24: Tagging or Record of Defective Equipment
Module 11
<number>
Power Brake Defects
Tag or card must be placed on the car at the time the defect is discovered and appear on both sides of the defective equipment. In lieu of a tag or card, the railroad may use an automated tracking system. In either case, the following information must be recorded on the record;
  The reporting mark and car or locomotive number,
  The name of inspection railroad,
  The name of inspector,
  The inspection location and date,
  The nature of each defect,
  The destination of defective equipment (repair point),
  The signature, if possible, and job tile of the person reporting the defective condition.

## Slide 25: Automated Tracking System
Module 11
<number>
Must be accessible for review at anytime by FRA or railroad employees
Automated system must be secure, contain the information from the previous slide, adequately track and monitor the movement of defective equipment
Failure to comply with these requirements could lead to FRA revoking the railroads option of using an automated tracking system
Notes: Module 11
<number>
Last bullet – if revoked it’s done in writing and will state the basis for the action. Probably something that will be processed by HQ.

## Slide 26: Operating Restrictions Defective Brakes
Module 11
<number>
Varies depending on total number of operative brakes in train and type of train
Operating restrictions required in order for movement to made without civil penalty liability

## Slide 27: Computation of Percent Operative Brakes
Module 11
<number>
A train equipped with disc brakes only, or with a combination of disc and tread braking units, determine percentage of operative power brakes in train by dividing the number of axles with operative brakes by total number of axles.
For trains equipped only with tread braking units (TBUs), divide number of operative TBUs by total number of TBUs
Each cut-out axle on a locomotive that weighs more than 200,000 pounds shall be counted as two cut-out axles for the purposes of calculating the percentage of operative brake

## Slide 28: Disk and Tread Brakes
Module 11
<number>
If an axle is equipped with both disk and tread brakes, and if either disk or tread brake is inoperative, that axle is considered to have inoperative brakes.

## Slide 29: Other Brake Defects
Module 11
<number>
The following brake defects should not be considered when calculating percentage of operative brakes in a train;
Failure or cutting out secondary brake systems,
Handbrakes or parking brakes,
Excessive piston travel that does not render brakes ineffective,
Brakes overdue for inspection, testing, maintenance, or stenciling.

## Slide 30: Operating Restrictions All Passenger Trains
Module 11
<number>
All passenger trains developing 50 to 74 percent operative power brakes may be used only as follows;
  The train may be moved in passenger service only to the next forward passenger station,
  The speed of the train shall be restricted to 20 mph or less, and
  After all passengers are discharged, the defective equipment shall be moved to the nearest location where the necessary repairs can be made.
Notes: Module 11
<number>

## Slide 31: Operating Restrictions 75 to 84 Percent Operative Brakes
Module 11
<number>
Commuter, short-distance intercity, and short-distance Tier II passenger trains with 75 to 84 percent operative brakes must;
  Reduce train’s maximum allowable speed by 50 percent or 40 mph, whichever is less,
  Moved to next forward location where repair can be made,
  If passenger safety is at risk, move the train to the next forward passenger station where passengers can be safely unloaded,
  After passengers are discharged, train must be moved to nearest location for repair.
Notes: Module 11
<number>
The train may be moved in passenger service only to the next forward location where the necessary repairs can be made; however, if the next forward location where the necessary repairs can be made does not have the facilities to handle the safe unloading of passengers, the train may be moved past the repair location in service only to the next forward passenger station in order to facilitate the unloading of passengers;

## Slide 32: Operating Restrictions 85 to 99 Percent Operative Brakes
Module 11
<number>
Commuter, short-distance intercity, and short-distance Tier II Passenger trains with 85 to 99 percent operative brakes must;
  Moved to next forward location where repair can be made,
  If passenger safety is at risk, the train may move to the next forward passenger station where passengers can be safely unloaded,
  After passengers are discharged, train must be moved to nearest location for repair.
Notes: Module 11
<number>
The train may be moved in passenger service only to the next forward location where the necessary repairs can be made; however, if the next forward location where the necessary repairs can be made does not have the facilities to handle the safe unloading of passengers, the train may be moved past the repair location in service only to the next forward passenger station in order to facilitate the unloading of passengers; and
238.15(d)(3)(ii)(B)
After all passengers are discharged, the defective equipment shall be moved to the nearest location where the necessary repairs can be made.
238.15(d)(4)

## Slide 33: Operating Restrictions
Module 11
<number>
Long distance intercity passenger trains with 75 to 84 percent operative brakes must;
  Reduce train’s maximum allowable speed by 50 percent or 40 mph, whichever is less,
  Moved to next designated forward location where repair can be made,
  If passenger safety is at risk, move the train to the next forward passenger station where passengers can be safely unloaded,
  After passengers are discharged, train must be moved to nearest location for repair.
Notes: Module 11
<number>
Sunset Limited, etc.

## Slide 34: Operating Restrictions
Module 11
<number>
Long distance intercity passenger trains with 85 to 99 percent operative brakes must;
  Moved to next designated forward location where repair can be made,
  If passenger safety is at risk, move the train to the next forward passenger station where passengers can be safely unloaded,
  After passengers are discharged, train must be moved to nearest location for repair.

## Slide 35: Operating Restrictions All Passenger Trains
Module 11
<number>
All passenger trains with completely inoperative power brakes on the front or rear unit and the handbrake is located inside the car, the following conditions apply;
  Qualified person must be stationed at handbrake,
  Car must be locked-out & empty (no passengers),
  Appropriate speed restrictions must be placed on train by qualified person.

## Slide 36: Operating Restrictions All Passenger Trains
Module 11
<number>
All passenger trains with completely inoperative power brakes on the front or rear unit and the handbrake is located outside the car or otherwise inaccessible , the following conditions apply;
  Car must be locked-out & empty (no passengers),
  Train shall be operated at restricted speed not to exceed 20 mph,
  The car shall be removed from the train or repositioned in the train at the first location where it is possible to do so.

## Slide 37: Movement of Defective Equipment Discussion
Module 11
<number>
Refer to matrices

## Slide 38: End of Module 5
Module 11
<number>