## Slide 1
Safety Culture:
Where have we been?
Where are we now?
Where are we going?
Michael Coplen
Michael Zuschlag
Joyce Ranney
Notes: <number>
Approx. 10 years ago FRA began investigating organizational culture. Subsequent reorganization of Volpe and HF Program to include Org. Culture & Safety Performance program.
This is a summary of FRA field evaluations of the impact of 4 innovative safety processes on safety culture. The evaluations were conducted within the Organizational Culture and Safety Performance program that seeks to identify, demonstrate, evaluate, and document effective approaches for improving safety and safety culture in the railroad industry. The program then stimulates adoption of effective approaches across industry.
Safety Culture Definition: “Shared values (what is important) and beliefs (how things work) that interact with an organization’s structures and control systems to produce behavioral norms (the way we do things around here)” (Reason, 1997)

## Slide 2: New Safety Approaches / New Safety Culture
Labor & management cooperation and commitment
Systematic, objective risk data collection and reporting
Preventative corrective actions
Problem-solving non-punitive confidential process
Notes: The safety approaches all instantiate changes to the safety culture by having these features that are not the traditionally characteristic of how the railroad industry handles safety.

## Slide 3: Pilot Demonstrations of Safety Approaches
FRA Presentation to TRB December, 2009
<number>
Approach | Carriers | Start
Participative Safety Rules Revision | ACBL, CSXT, KCS, CN-IC | 1999
Investigation of Safety Related Occurrences Protocol (ISROP) | Canadian Pacific | 2003
Clear Signal for Action (CSA) | Amtrak, Union Pacific | 2001
Confidential Close Call Reporting System (C3RS) | Union Pacific, Canadian Pacific | 2007
Notes: <number>
ISROP & Participatory were industry-initiated.

## Slide 4: Participative Safety Rules Revision – OVERVIEW
FRA Presentation to TRB December, 2009
<number>
Safety Rules
Notes: <number>
In participative rules revision (or rules consolidation)
Labor and management jointly identify universally enforceable rules
Eliminate unnecessary and conflicting rules
Involves a shift in primary responsibility for rules creation from management to front-line workers with management in a support role
Safety Rules Revision conducted at three railroad carriers and one in-land barge carrier. As shown in the graph above, each carrier substantially consolidated numerous safety rules, policies, job aids, and training information (some craft specific and some for general use) to a smaller number of core and craft-specific rules.
American Commercial Barge Lines
CSXT
Kansas City Southern
Canadian National - Illinois Central

## Slide 5: Participative Safety Rules Revision – RESULTS
FRA Presentation to TRB December, 2009
<number>
Significant Incident Rate Reduction at One Railroad
Notes: <number>
FINDINGS:
Kansas City Southern (KCS) showed a statistically significant reduction in incidents following implementation of the safety rule revisions.
Two carriers reported significant reductions in the number of liability claims related to the Federal Employer’s Liability Act (FELA) and the cost per claim.
Across all sites, interviewees reported increased rule compliance and that this was because the workforce valued the new rulebooks.

## Slide 6: ISROP – OVERVIEW
FRA Presentation to TRB December, 2009
<number>
Corrective
Actions
Workforce
Presentation
System-wide
Communication
Joint Labor-
Mgt Team
Root-Cause
Analysis
Safety Occurrences
ISROP: Investigation of Safety Related Occurrences Protocol
Notes: <number>
Investigation of Safety Relate Occurrences Protocol
A joint management-labor process for investigating accidents and close-calls in order to identify the root causes.
Once causes are identified, workers are warned of the issue through safety briefings and system-wide communications.
A team also seeks to implement corrective actions to remove the causes.

## Slide 7: Injuries Reduced as Substantial Numbers of ISROPs Accumulate
FRA Presentation to TRB December, 2009
<number>
 | Total number of ISROPs | Correlation Coefficients
Site 1 | 142 | 0.21*
Site 2 | 114 | 0.20*
Site 3 | 7 | 0.03
Corresponds to 50% decrease in injury rate
*p < 0.05
Notes: <number>
<number>
ISROP was implemented in the mechanical departments at CPR at three different study sites across the continent.
The three sites have comparable number of employees, but the number of total ISROPs conducted varied considerably for the three sites
Site 1, for example, included close calls in its investigations, while Site 3 limited ISROPS to only severe accidents)
At the two sites which did a lot of ISROPs, the time between each injury increased as ISROPs accumulated. This trend didn’t happen at the site which did only a few ISROPs.
In this case, a correlation coefficient of 0.21 corresponds to cutting the rate of injuries were cut in half.
We can conclude that Site 1 is significantly different from 3 (z = 2.015, p < 0.05). 2 and 3 also show a significant difference (z = 1.93, p < 0.05). But 1 is very similar to 2 and there is no significant difference between them (z = 0.14, p = 0.88).
In a culture survey, the 2 sites with more ISROPs were also perceived by workers to have greater improvements investigation effectiveness.
[[consider getting corresponding % decrease all rows. Focus notes there. Maybe even eliminate r’s?

## Slide 8: Clear Signal for Action (CSA) OVERVIEW
FRA Presentation to TRB December, 2009
<number>
Safety
Outcomes
Workers
Observation & Feedback to Peers
Workers
Collect Behavioral Explanations
Joint Team
Analyze Trends in Explanations
Joint Team
Develop Corrective Actions
Managers
Support and Participate
Behavior-based Safety
Continuous Improvement
Safety Leadership Development
Notes: <number>
The three components of CSA have been shown in other industries to be effective at proactively improving safety. The components work together like this:
Behavior-based Safety (BBS). Peer-to-peer observations and feedback, where trained workers systematically observe and discuss safe practices with other workers. The idea is that such discussion encourages workers to reflect on their behavior, which should yield internalization of safer practices.
2. Continuous Improvement (CI). Workers and managers work together to analyze the data on risky behaviors seen during observations for systemic causes (barriers to safety), and work out corrective actions. This may include things like feedback, worker education and training, policy changes, workplace maintenance or enhancements.
3. Safety Leadership Development (SLD). Managers are trained to more effectively support safety and safety programs through methods other than discipline.
By systematically identifying and correcting behaviors and conditions that increase the risk of accidents, this method aims to prevent accidents before any occur.

## Slide 9: Clear Signal for Action RESULTS
FRA Presentation to TRB December, 2009
<number>
Site | Department | Outcomes
Amtrak – Chicago | Station Services (Hi Supervision) | 80% drop in injury rates
Union Pacific – Louisiana | Switching (Moderate Supervision) | 62% drop in human-factors yard derailments
Union Pacific – San Antonio | Road (Lo Supervision) | 72% drop in locomotive engineer decertification rates
Notes: <number>
CSA pilots have been demonstrated at Union Pacific (two sites: San Antonio and Louisiana) and Amtrak (Chicago Terminal Services).
Amtrak (EAGLES):
80% drop in injury rates (all injuries) in a station services department compared to the year before all-hands training on BBS checklist to the year after training
Includes 76% drop in reportable injuries. This drop in injuries corresponded to a $300,000 projected annual savings for a full CSA implementation.
UP Louisiana (STEEL)
The rate of incidents (mostly derailments) in yards attributed to human factors cut by nearly two thirds . Comparison yards without CSA in Louisiana showed no such improvements
Also interviews indicate improved safety awareness, labor-management relations and barrier removals.
UP San Antonio (CAB)
72% drop in locomotive engineer de-certification rates for speed, stop, and main-track authority violations. Comparison service units without CSA in the region showed no such improvement
These decerts were hypothesized to be associated with this particular CSA implementation. For decerts not associated with the CSA process, there is no trend. For a four-year baseline prior to 9/05, all services units showed no significant linear trend in decertifications.
San Antonio also had a smaller switching-based CSA process which showed a 69% reduction in human factors yard derailment rates, much like seen in Louisiana.
San Antonio also had statistically significant improvements in labor management relations.

## Slide 10: Confidential Close Call Reporting System (C3RS) – OVERVIEW
FRA Presentation to TRB December, 2009
<number>
Worker
Report sent to C3RS system
Government Data analysis and report
Joint Labor Manage Team
Problem-solve
Site
Implements safety change
Safety Occurrences
Notes: <number>
Confidential Close Call Reporting System (C3RS) is a program where employees at a site voluntarily and confidentially report events that could result in accidents but did not. These reports are compiled from multiple carriers into a Bureau of Transportation Statistics (BTS) government-protected database. BTS analyzes the data for trends and returns reports on these the site.
At the site, managers and workers work together to understand why these events occur, identify corrective actions to prevent them. The site then implements the corrective actions, reducing the chance of future close calls and accidents of that type.
Accidents are usually preceded by close calls, so they are early warnings of safety problems. C3RS uncovers hidden at-risk conditions not previously exposed from analysis of reportable accidents and incidents. Analysis of close-calls data serves as a new tool for identifying and proactively managing risk.
Close Call Definition: “An opportunity to improve safety practices based on a condition, or an incident with a potential for more serious consequences.”
This is the latest demonstration in the Organizational Culture and Safety Performance program, so it’s too soon to know the impacts on safety. But there are some hints that it is having an impact:
At one site, an FRA analysis found that accident rates attributed to human factors have declined 67 percent. By comparison, across all railroads, the overall reduction in accidents was 18 percent for the same period, but we’re not sure yet if this is the proper comparison
Injury rates transportation workers has declined by 23 percent.
Reports are coming in at a rate of 10.5 per week, thanks to assurances of confidentiality, so there is at least an opportunity to see if it will have an impact.

## Slide 11: Safety Culture Going Forward
FRA Presentation to TRB December, 2009
<number>
Organization | Policy Changes
FRA | RSA, 2008. New Risk Reduction division 6 new Risk Reduction pilots so far
Union Pacific | System-wide safety culture change
Toronto Transit | System-wide safety culture change
Amtrak | System-wide safety culture change Joining C3RS
Canadian Pacific | Re-committed to ISROP
New Jersey | Joining C3RS
Notes: <number>
These four pilot demonstrations constitute the start of a cultural transformation in how railroads approach safety. As the success of these approaches are demonstrated and disseminated, policy changes are being effected in railroad industry and regulation, turning more to these proactive non-punitive cooperative data-based approaches to safety.
Government: Legislation funds new risk reduction division. FRA issues Broad Agency Announcement offering sponsorship of risk reduction approaches like those discuss here. They’ve initiated 6 risk-reduction industry pilots so far.
UP – Joined C3RS as CSA pilots appeared to be successful. Implementing CSA-like Total Safety Culture effort in all transportation and mechanical at all service units.
Toronto Transit - Full org/safety culture change,
Amtrak – System-wide safety culture effort. Includes joining C3RS.
CP – ISROP stimulates policy changes, recommitted to continue
New Jersey Transit - Joining C3RS.

## Slide 12: Next Steps for FRA R&D
FRA Presentation to TRB December, 2009
<number>
Complete cross-site evaluations
Develop communications plan
Disseminate evaluation results
Notes: <number>
FRA R&D Next Step:
Continue evaluation of C3RS demonstration.
Communication plan to inform industry of effectiveness of these safety approaches

## Slide 13: Acknowledgments
The workers and managers at:
  Amtrak
  Union Pacific
  Canadian Pacific
  American Commercial Barge Lines
  CSX
  Kansas City Southern
  Canadian National - Illinois Central
The members and leaders of
  United Transportation Union
  Brotherhood of Locomotive Engineers and Trainmen
  Transportation Communication Union
  Canadian Auto Workers
  Teamsters
  Brotherhood of Railway Carmen
The consultants, evaluators, & researchers at:
  Behavioral Science Technology
  Bureau of Transportation Statistics
  University of Connecticut Industrial Psychology Applications Center
  NewVectors
  WreathWood Group
  MacroSys
  Chenega Advanced Solutions & Engineering, LLC
  Western Michigan University Evaluation Center
  EG&G Technical Services
  The Hile Group